specifications.

The USB host controllers have their own specifications. With USB 1.1, there were two Host Controller Interface Specifications, UHCI (Universal Host Controller Interface) developed by Intel which puts more of the burden on software (Microsoft) and allowing for cheaper hardware and the OHCI (Open Host Controller Interface) developed by Compaq, Microsoft and National Semiconductor which places more of the burden on hardware(Intel) and makes for simpler software.

With the introduction of USB 2.0 a new Host Controller Interface Specification was needed to describe the register level details specific to USB 2.0. The EHCI (Enhanced Host Controller Interface) was born. Significant Contributors include Intel, Compaq, NEC, Lucent and Microsoft so it would hopefully seem they have pooled together to provide us one interface standard and thus only one new driver to implement in our operating systems.

USB supports plug’n’plug with dynamically loadable and unloadable drivers. The user simply plugs the device into the bus. The host will detect this addition, interrogate the newly inserted device and load the appropriate driver all in the time it takes the hourglass to blink on your screen provided a driver is installed for your device. The end user needs not worry about terminations, terms such as IRQs and port addresses, or rebooting the computer. Once the user is finished, they can simply lug the cable out, the host will detect its absence and automatically unload the driver.
The loading of the appropriate driver is done using a PID/VID (Product ID/Vendor ID) combination. The VID is supplied by the USB Implementor's forum.